## Slide 1: Yggdrasil (for Sensor Addition)
Flask(software dev.)

## Slide 2: 개요
Yggdrasil Sensor Component를 추가하는 방법을 채계적이고 쉽게 설명하기 위해서 만듬

## Slide 3: 설정
센서이름 : Dummy
Type Number : 250 (0xFA)
RF Interval : 1024(1초)
기능 : Pin 제어
      Uart 제어
      Multihop RF 통신

## Slide 4: Makefile
CFLAGS += -DDUMMY
CFLAGS += -I./Sensor/250Dummy
UART 사용하는 경우
CFLAGS += DDEFAULT_BAUDRATE=9600

## Slide 5: Yggdrasil.h
(Sensor Type)
DUMMY_OSCILLOSCOP = 250
(Sensor RF Interval)
DUMMY_INTERVAL = 1024U
typedef nx_struct dummy_oscilloscope{
base_info_t info;
nx_uint8_t data[4];
} dummy_oscilloscope_t;

## Slide 6: YggdrasilAppC.nc
#elif DUMMY
#warning ##### DUMMY SENSOR ###
Components DummySensorC as SensorC;

## Slide 7: Sensor 추가
Yggdrail/Sensor 폴더로 간다.
- 250Dummy 폴더를 생성한다.
- DummySensorC.nc 파일을 생성한다.
- DummySensorP.nc 파일을 생성한다.
Tip : Dummy : Uart + Pin + RF Commponent

## Slide 8: Sensor/DummySensorC.nc
components new CollectionSenderC(DUMMY_OSCILLOSCOPE);

## Slide 9: Sensor/DummySensorP.nc
dummy_oscilloscope_t local;
local.info.type = DUMMY_OSCILLOSCOPE;
setTimer(DUMMY_INTERVAL);
dummy_oscilloscope_t * out =
(dummy_oscilloscope_t *)call Send.getPayload(&sendbuf, sizeof(dummy_oscilloscope_t));
local.data[0] = 0x11;
local.data[1] = 0x33;

## Slide 10: Sensor/BaseC.nc
BaseP.DUMMYRev -> Collector.Receive[DUMMY_OSCILLOSCOPE];

## Slide 11: Sensor/BaseP.nc
Interface Receive as DUMMYRev;
event message_t* DUMMYRRev.receive(message_t* msg,
void *payload,
uint8_t len){
return receive(DUMMY_OSCILLOSCOPE, msg, payload, len);
}
else if(type == DUMMY_OSCILLOSCOPE){
uartlen = sizeof(dummy_oscilloscope_t);
}

## Slide 12: 확인